TEXAS GENERAL LAND OFFICE

Community Development Block Grant (CDBG)

Disaster Recovery Program

| Initial Inspection Checklist |
| --- |
| Subrecipient Name | Contract # |
| Household Name | Activity # |
| Household Address |

| Total Enclosed Square Feet: |  |
| --- | --- |
| Describe Assisted Properties Structural Deficiencies |

DIRECTIONS: Examine each inspection item. Check off each box individually in the PASS/FAIL column for each inspection item. If item fails, describe the scope of work required to repair the item. Accurate measurements and quantities of materials should be included. After inspection is complete, sign and date form on last page of check list. Unsigned or incorrectly filled Inspection Checklists will be considered incomplete.

| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| --- | --- | --- | --- |
| GENERAL HEALTH AND SAFETY |
| Access to Unit (HQS 52580 8.1): Can the unit be accessed without having to enter through another unit? |  |  |  |
| Exits (HQS 52580 8.2): Is there an adequate fire exit from this building that is not blocked? |  |  |  |
| Do all rooms that are used for living have fire exits? |  |  |  |
| Evidence of Infestation (HQS 52580 8.3): Is the unit free from severe infestations of rats, mice, or vermin? |  |  |  |
| Is there any kind of insect infestation apparent? |  |  |  |
| Is there evidence of termite infestation? |  |  |  |
| Garbage and Debris (HQS 52580 8.4): Is the unit free from heavy accumulation of garbage or debris inside and outside? (include all enclosed areas, porches, out-buildings, and yards) |  |  |  |
| Refuse Disposal (HQS 52580 8.5): Are there adequate covered facilities for temporary storage and disposal of waste (i.e. garbage cans) and are they approvable by any applicable jurisdiction? |  |  |  |
| Is there a regular method of waste removal? |  |  |  |
| Interior Stairs and Common Halls (HQS 52580 8.6): Are all stairs and walkways free from hazards to the occupant (i.e. no loose, broken, or missing steps on stairways, absent or insecure railing, inadequate lighting or other hazards)? |  |  |  |
| Other Interior Hazards (HQS 52580 8.7): Is the unit free from any interior hazards not specifically identified in this list? |  |  |  |
| Elevators (HQS 52580 8.8): Are all elevators in safe working condition If not applicable, indicate N/A. |  |  |  |
| Where local practice requires, do all elevators have a current inspection certificate? If not applicable, indicate N/A, |  |  |  |
| Interior Air Quality (HQS 52580 8.9): Is the interior of the unit free from abnormally high levels of air pollution from vehicular exhaust, sewer gas, fuel gas, dust, or other pollutants? |  |  |  |
| Site and Neighborhood Conditions (HQS 52580 8.10): Is the site and the immediate neighborhood free from conditions which would seriously and continuously affect the health and/or safety of the residents? |  |  |  |
| Lead-Based Paint (HQS 52580 8.11): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| BUILDING EXTERIOR |
| Condition of Foundation (HQS 52580 6.1): Is foundation is sound and free from hazards? |  |  |  |
| What type of foundation is apparent? |  |  |  |
| If the foundation is a slab, is it free from cracks evident in the interior or on the exposed exterior? |  |  |  |
| If the foundation is pier-and-beam, is there adequate clearance to observe all piers, sills, joist and other foundations members and has this been done? |  |  |  |
| Maximum spans should be 9’6” assuming 2x6 joist and 4’6” beams and sills. |  |  |  |
| If the foundation is a pier-and-beam, there should be adequate pier placements to support the house and piers should be of proper design (cinder block which is not reinforced with concrete/steel should not be used for new installation). Refer to SBCCI/CABO. |  |  |  |
| If leveling is required, draw the exact placement and design of all piers. Will this level the house or simply provide adequate support? Inform home owner and get approval in writing. |  |  |  |
| All beams, sills, joist, blocks are properly supported. |  |  |  |
| All beams, sills, joist, blocks are free from termites or rot. |  |  |  |
| Is the underpinning, if any, adequate? Is it properly installed, sealed, and unbroken? Is it vented and insulated as needed? Note any needed repairs. |  |  |  |
| Grade should be sloped away from foundation. No voids or depressions should be apparent. |  |  |  |
| There should be no standing water beneath or adjacent to the foundation. |  |  |  |
| Condition of Stairs, Rails, and Porches (HQS 52580 6.2): Condition of stairs, rails, and porches should be free from hazards and structural defects. Detail any required carpentry repairs. |  |  |  |
| If more than 2 steps are present, a hand rail is required. If more than 2 steps are present, is a hand rail installed? |  |  |  |
| Is the porch floor sound and free from rot or other deterioration? |  |  |  |
| All private and public walkways should be free from tripping hazards and other serious defects. Note any flat work repairs needed. Include measurements. |  |  |  |
| Condition of Roof/Gutters (HQS 52580 6.3): Are the roof, gutters, and down spouts sound and free from hazards? |  |  |  |
| Are all vent jacks, leads, turbines, skylights and caps in good condition? |  |  |  |
| Is there any buckling or sagging evident in the roof surface? |  |  |  |
| Inspect the interior of the attic space and the underside of eaves paying careful attention to valleys and penetrations. Are any leaks evident? |  |  |  |
| Note the type of decking and the number of layers of shingles. No more than 2 layers are acceptable. If tear off is necessary, estimate the amount of decking, if any, required. |  |  |  |
| Roof should be free from incipient deficiencies. Will it last at least five more years given normal conditions? |  |  |  |
| Check all soffits, look-outs and fascia for damage. Estimate repair area. |  |  |  |
| Inspect attic space for adequate roof support. Note any requirement for additional purlines, jacks, collars, or other support. (Note any additional attic items included in other parts of the checklist, insulation, plumbing, electrical, infestation, etc.) |  |  |  |
| Are all gutters free from debris and in working order? |  |  |  |
| Are additional gutters required? Gutters should only be required where water needs to be pulled away from the house or walkways? |  |  |  |
| Condition of Exterior Surfaces (HQS 52580 6.4): Are exterior surfaces sound and free from hazards? |  |  |  |
| Are all surfaces free from holes, gaps, open seams and incursions allowing thermal or water leaks into the interior? |  |  |  |
| Is any rot or termite damage evident? Check all surfaces including soffit, fascia, eaves, siding, water tables, decks, porch floors, etc.? If rot is present, calculate the square area and types of surface and structure damage. |  |  |  |
| Is any condition evident that would encourage rot or termite damage? Do any surfaces collect or trap water? Does any untreated wood have contact with the ground? These issues should be considered incipient deficiencies. |  |  |  |
| Check exterior trim including all window sills and door jambs for damage and proper sealing. |  |  |  |
| Are any exterior masonry repairs required? |  |  |  |
| Are windows in working order, free from rot, and sealed? Replace any cracked or missing panes and re-caulk any areas with dry, cracked or missing caulk. |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Estimate the amount of glass, if any, requiring replacement. |  |  |  |
| If window units require replacement, note location, measured size, and type of unit to be installed. |  |  |  |
| Is the unit free from any exterior hazards not specifically identified in this list? |  |  |  |
| Electric service should be of three-wire type with weather-head located at least 12’ from grade. |  |  |  |
| Service panel should have a service rating and a disconnect present for at least 100 amps for existing and 150 amps for any new installation. All installations shall meet the N.E.C. |  |  |  |
| Disconnects for HVAC condensing units should be located within reach of unit. |  |  |  |
| All exterior entrances must include a light fixture controllable from the interior. |  |  |  |
| Condition of Chimney (HQS 52580 6.5): Is chimney sound and free from hazards? |  |  |  |
| Lead-Based Paint Exterior Surfaces (HQS 52580 6.6): Are all exterior surfaces free from cracked, peeling, and chipping paint? |  |  |  |
| If not, do deteriorated surfaces exceed 20 square feet of total exterior surface area? |  |  |  |
| Manufactured Housing Unit (MHU) (HQS 52580 6.7): If the unit is a manufactured housing unit, is it properly tied down and placed? |  |  |  |
| If the unit is a manufactured housing unit, does it have at least 1 smoke detector outside each bedroom? |  |  |  |
| Is the underpinning, if any, adequate? Is it sealed and unbroken? Is it vented and insulated as needed? |  |  |  |
| ATTIC |
| Can the attic be accessed? |  |  |  |
| When possible, attic should include R30 insulation. Estimate R value of attic insulation and note additional insulation requirements. |  |  |  |
| Check for exposed wiring including knob-and-tube and replace. All wiring should be properly shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| LIVING ROOM |
| Living Room Present (HQS 52580 1.1): Is there a living room? |  |  |  |
| Electricity (HQS 52580 1.2): Are there at least 2 working outlets or at least 1 working outlet and 1 light fixture? |  |  |  |
| Are the outlets properly grounded and in working order? |  |  |  |
| Electrical Hazards (HQS 52580 1.3): Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 1.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable and lockable (where required) condition? |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 1.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 1.6): Is the ceiling sound and free from hazardous defects |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 1.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 1.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 1.9): Is there evidence of lead-based paint? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other: Are there any other unusual features present? (i.e. low ceilings, angled or narrow spaces, cantilevered loads, etc.) |  |  |  |
| KITCHEN |
| Kitchen Area Present (HQS 52580 2.1): Is there a kitchen? |  |  |  |
| Electricity (HQS 52580 2.2): Do any outlets which are 6 feet or less measurable to the nearest source of standing (sinks or tubs) or running water have properly installed and functioning GFCI outlets? |  |  |  |
| Is there at least 1 working outlet and at least 1 working and permanently installed light fixture? |  |  |  |
| Electrical Hazard (HQS 52580 2.3): Are all outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 2.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 2.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 2.6): Is the ceiling sound and free from hazardous defects |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 2.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 2.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 2.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| Stove or Range with Oven (HQS 52580 2.10): Is there a working oven and a stove (or range) with top burners that work? |  |  |  |
| Refrigerator (HQS 52580 2.11): Is there a working refrigerator that maintains a temperature low enough so that food does not spoil over a reasonable period of time? |  |  |  |
| Sink (HQS 52580 2.12): Is there a sink that works and provides hot and cold running water? |  |  |  |
| Is the sink attached and sealed properly to prevent movement or leaks? Is it free from holes, rust, or cracks? |  |  |  |
| Do the faucets work properly? Check for leaks, free operation, proper water mixing, and complete shut off. |  |  |  |
| Are the drain lines properly installed with working, un-deteriorated p-traps (check for leaks and proper rate of draining), and is the system properly vented? |  |  |  |
| Are supply lines properly installed and not leaking? |  |  |  |
| Are hot and cold water shut off valves present and working properly? |  |  |  |
| Check hot water heater installation and operation. |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Are all counter surfaces level, properly fastened, free from de-lamination, washable and free from deterioration? |  |  |  |
| Are all cabinet doors in working order, properly hinged, closable, and free from deterioration? |  |  |  |
| Are all cabinet shelves and backs level, usable and free from deterioration? |  |  |  |
| In general, are the cabinets properly fastened to the walls and in good usable condition? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other: Are there any other unusual features present? (i.e. low ceilings, angled or narrow spaces, cantilevered loads, etc.) |  |  |  |
| BATHROOM |
| Bathroom (HQS 52580 3.1): Is there a bathroom? |  |  |  |
| Electricity (HQS 52580 3.2): Is there at least 1 permanently installed and working light fixture? |  |  |  |
| Electrical Hazards (HQS 52580 3.3): Do any outlets which are 6 feet or less measurable to the nearest source of standing (sinks or tubs) or running water have properly installed and functioning GFCI outlets? |  |  |  |
| Are all outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 3.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 3.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 3.6): Is the ceiling sound and free from hazardous defects |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 3.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 3.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 3.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| Flush Toilet in Enclosed Room in Unit (HQS 52580 3.10): Is there a working toilet in the unit in an enclosed room for the exclusive private use of the resident? |  |  |  |
| Check the toilet for operation. Does it flush freely and completely? |  |  |  |
| Does the flapper seal properly? Shut off all water sources and check for meter movement. |  |  |  |
| Is the supply line working properly and is it free from leaks? Check the float system operation. |  |  |  |
| Is there a working shut off valve? (drain toilet and check operation) |  |  |  |
| Is the toilet properly secured to the floor? |  |  |  |
| Check all other seals for leaks, wax ring/flange, tank/bowl, supply lines, etc. |  |  |  |
| Check floor for water damage. |  |  |  |
| Are the seat and lid in good repair? Are they securely attached? |  |  |  |
| Fixed Wash Basin or Lavatory in Unit (HQS 52580 3.11): Is there a working permanently installed wash basin with hot and cold running water? |  |  |  |
| Is the basin attached and sealed properly to prevent movement or leaks? Is it free from holes, rust, or cracks? |  |  |  |
| Do the faucets work properly? Check for leaks, free operation, proper water mixing, and complete shut off. |  |  |  |
| Are the drain lines properly installed with working, un-deteriorated p-traps (check for leaks and proper rate of draining), and is the system properly vented? |  |  |  |
| Are supply lines properly installed and not leaking? |  |  |  |
| Are hot and cold water shut off valves present and working properly? |  |  |  |
| Check faucets for proper hot water flow. |  |  |  |
| Tub or Shower in Unit (HQS 52580 3.12): Is there a working tub or shower with hot and cold running water in the unit? |  |  |  |
| Is the tub/shower attached and sealed properly to prevent movement or leaks? Is it free from holes, rust or cracks? |  |  |  |
| Do the bath faucets work properly? Check for leaks, free operation, proper water mixing and complete shut off. |  |  |  |
| Are the drain lines properly installed with working un-deteriorated p-traps (check for leaks and proper rate of draining), and is the system properly vented? |  |  |  |
| Are supply lines properly installed and not leaking? |  |  |  |
| Check for proper hot water flow to bath. |  |  |  |
| Ventilation (HQS 52580 3.13): Are there openable, operable windows or a working ventilation system? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other: Are there any other unusual features present? (i.e. low ceilings, angled or narrow spaces, cantilevered loads, etc.) |  |  |  |
| Other Room Used for Living and Halls (include Bedrooms) - #1 (HQS 52580 4.1): Room Location: Right/Left/Center of unit Front/Rear/Center of unit Floor Level |
| Electricity/Illumination (HQS 52580 4.2): Are there at least 2 working outlets, or at least 1 working outlet and 1 permanently installed light fixture? |  |  |  |
| Electrical Hazards (HQS 52580 4.3): Are the outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 4.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 4.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 4.6): Is the ceiling sound and free from hazardous defects? |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 4.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 4.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Lead-Based Paint (HQS 52580 4.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other: Are there any other unusual features present? (i.e. low ceilings, angled or narrow spaces, cantilevered loads, etc.) |  |  |  |
| Other Room Used for Living and Halls (include Bedrooms) - #2 (HQS 52580 4.1): Room Location: Right/Left/Center of unit Front/Rear/Center of unit Floor Level |
| Electricity/Illumination (HQS 52580 4.2): Are there at least 2 working outlets, or at least 1 working outlet and 1 permanently installed light fixture? |  |  |  |
| Electrical Hazards (HQS 52580 4.3): Are the outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 4.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 4.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 4.6): Is the ceiling sound and free from hazardous defects? |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 4.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Inspection Item | Pass | Fail | Scope of Work Required Include measurements and quantities |
| Floor Condition (HQS 52580 4.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 4.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other Room Used for Living and Halls (include Bedrooms) - #3 (HQS 52580 4.1): Room Location: Right/Left/Center of unit Front/Rear/Center of unit Floor Level |
| Electricity/Illumination (HQS 52580 4.2): Are there at least 2 working outlets, or at least 1 working outlet and 1 permanently installed light fixture? |  |  |  |
| Electrical Hazards (HQS 52580 4.3): Are the outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 4.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 4.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and is it free from severe deterioration or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 4.6): Is the ceiling sound and free from hazardous defects? |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 4.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 4.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 4.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| If not, do deteriorated surfaces exceed 2 square feet per room and/or is more than 10% of a component? |  |  |  |
| Smoke Alarm: Is there a working smoke alarm for this room? There should be a smoke alarm adjacent to every sleeping area. |  |  |  |
| Does the smoke detector meet the requirements of NFPA 74? |  |  |  |
| In units occupied by the hearing impaired, is there an alarm system connected to the smoke detector? |  |  |  |
| Other Room Used for Living and Halls (include Bedrooms) - #4 (HQS 52580 4.1): Room Location: Right/Left/Center of unit Front/Rear/Center of unit Floor Level |
| Electricity/Illumination (HQS 52580 4.2): Are there at least 2 working outlets, or at least 1 working outlet and 1 permanently installed light fixture? |  |  |  |
| Electrical Hazards (HQS 52580 4.3): Are the outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Security (HQS 52580 4.4): Are all windows in openable, operable, and lockable condition? |  |  |  |
| Are all doors in openable, operable, and lockable (where required) condition? |  |  |  |
| Are all exterior doors equipped with workable deadbolts? |  |  |  |
| Are all exterior doors solid core? |  |  |  |
| Window Condition (HQS 52580 4.5): Are all windows and doors properly weather-stripped and sealed? |  |  |  |
| Is there at least 1 window and are all windows free from signs of severe deterioration or missing or broken panes? |  |  |  |
| Ceiling Condition (HQS 52580 4.6): Is the ceiling sound and free from hazardous defects? |  |  |  |
| Is the ceiling paint free from chipping or peeling? |  |  |  |
| Is the ceiling sagging indicating roof leaks or structural repairs? Indicate necessary structural repairs or refer to roof section. |  |  |  |
| Is the ceiling free from water stains, popped seams and cracking? Include any drywall repairs. |  |  |  |
| Wall Condition (HQS 52580 4.7): Are all walls framed? Check for single wall construction. |  |  |  |
| On exterior walls, check for insulation and estimate R-value. |  |  |  |
| Are all walls sound and free from hazardous defects? |  |  |  |
| Is the paint free from chipping or peeling? |  |  |  |
| Are the walls leaning? |  |  |  |
| Are the walls free from water stains, popped seams and cracking? |  |  |  |
| Floor Condition (HQS 52580 4.8): Are all baseboards and other trim properly sealed and in good condition? |  |  |  |
| Is there any evidence of sub-floor rot or termite damage? |  |  |  |
| Is the floor sound and free from hazardous defects? |  |  |  |
| Are any tripping hazards present? |  |  |  |
| Is the floor generally level? |  |  |  |
| Note the general condition of flooring materials. If replacement, repair, or cleaning is required, measure area of repair. |  |  |  |
| Lead-Based Paint (HQS 52580 4.9): Are all painted surfaces free of deteriorated paint? |  |  |  |
| All Secondary Rooms (Rooms not Used for Living) |
| Security (HQS 52580 5.2): Are all windows and doors that are accessible from the outside lockable in each room? |  |  |  |
| Electrical Hazards (HQS 52580 5.3): Are all rooms free from electrical hazards? |  |  |  |
| Are the outlets properly grounded and in working order? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Are any shorts, overloaded circuits, or frayed wires present? |  |  |  |
| Check for exposed wiring including knob-and-tube, and replace. All wiring should be shielded or conduited. All connections should be in approved j-boxes. |  |  |  |
| Are all outlet covers and switch plate covers properly installed and free from cracks or gaps? |  |  |  |
| Are all switches and outlets in working order and of a type of proper amperage rating and material for the circuit being inspected? No aluminum wiring or devices should be considered free of hazard. |  |  |  |
| Are there any other conditions not mentioned which would constitute an electrical hazard? |  |  |  |
| Other Potentially Hazardous Features in these Rooms (HQS 52580 5.4): Are all rooms free from any other potentially hazardous feature? Explain any hazard. |  |  |  |
| Heating and plumbing |
| Adequacy of Heating Equipment (HQS 52580 7.1): Is the heating equipment capable of providing adequate heat (either directly or indirectly) to all rooms used for living? |  |  |  |
| Can all living areas be heated to at least 68F in all conditions? |  |  |  |
| Safety of Heating Equipment (HQS 52580 7.2): Is the unit free from unvented fuel burning space heaters or any other types of unsafe heating conditions? |  |  |  |
| Are fuel supply tanks an adequate distance from the house and are all supply mains buried or concealed and properly attached under a properly vented crawl space? Is there an exterior shut off? |  |  |  |
| Are fuel supply lines in good non-leaking condition? |  |  |  |
| Are all unused interior shut offs removed and capped beneath the floor? |  |  |  |
| Are all heat exchangers, burners, and plenums free from rust or corrosion and in serviceable and safe condition? |  |  |  |
| Is the heater too large for the space in which it is used, thus creating a hazard? Is it installed near combustible material thus creating a hazard? |  |  |  |
| Are all working shut off valves updated to include no “Texas Trees” and does every appliance have an accessible shut off? |  |  |  |
| Ventilation/Cooling (HQS 52580 7.3): Are all heaters properly vented? |  |  |  |
| Is the vent system sealed to prevent leaks and free from blockage? |  |  |  |
| If an un-vented heater is used, it must have and ODS system and a U.I. tag indicating same. Does it? |  |  |  |
| Does the unit have adequate ventilation and cooling by means of openable windows or a working cooling system. |  |  |  |
| No more than 2 45-degree bends should be present in the venting system which should be of double walled vent stack. |  |  |  |
| Water Heater (HQS 52580 7.4): Is the water heater located, equipped, and installed in a safe manner? |  |  |  |
| Is a TPL valve properly installed and flowing water to the exterior of the building? |  |  |  |
| Is the water heater providing adequate hot water to the unit? |  |  |  |
| If the water heater is gas, propane or oil fired, is it at least ten inches from walls and properly vented with double walled vent pipe? Is combustion air supplied from the exterior? |  |  |  |
| If the water heater is located in an exterior closet, is it sealed to prevent freezing of lines? |  |  |  |
| Is a working water shut-off valve installed? |  |  |  |
| Is the home served by an approvable public or private water source? |  |  |  |
| Is a working gas shut-off installed? |  |  |  |
| Are leaks evident at the floor? Is the placement solid? Can you shake the water heater? |  |  |  |
| Water Supply (HQS 52580 7.5): Is the unit served by an approvable public or private sanitary water supply? |  |  |  |
| Are all water lines in good condition, free from corrosion and rust? |  |  |  |
| Are all lines properly secured? |  |  |  |
| Are all lines free from free hazard? |  |  |  |
| Is there an owner’s shut-off present and in working order? |  |  |  |
| Are all vents properly attached and of adequate height? |  |  |  |
| Is there evidence of vent blockage? |  |  |  |
| Are clean-outs available? |  |  |  |
| Is there any evidence of crushed lines or roots in the line? (interview the owner) |  |  |  |
| Is there any evidence of sewage leakage? |  |  |  |
| Plumbing (HQS 52580 7.6): Is the plumbing free from major leaks or corrosion that causes serious and persistent levels of rust or contamination of the drinking water? |  |  |  |

I certify that to the best of my knowledge and belief all of the information on this form is correct.

Inspector Signature Date of Inspection